Product Specification Sheet

SL1-200 DF

Flyable Two-Way Loudspeaker System

# General

The SL1-200 DF is an unique “solution oriented” Loudspeaker which bridges sound clarity and fidelity, and unparalleled pattern control with a venue aesthetic designed package that is also simple to install. The SL1-200 DF incorporates two superb geometrically designed and coaxially assembled asymmetrical horns with coverage parameters of 15 degrees in the upper vertical, 45 degrees in the lower vertical, and 110 degrees in the horizontal. The exceptionally designed and crafted HF horn is coupled to a 1” exit HF driver. A 12” transducer is coupled to a mid frequency asymmetrical horn.  These horn driver assemblies deliver energy where it’s precisely required - to the audience. The mid and hi frequency horns and drivers are controlled by an internal passive crossover. To assist in the always-problematic “front fill” two lower 90 degree horizontal coverage x 60 degree vertical pattern HF horn/driver assemblies are attached to adjustable mounts. These devices are controlled by a specific passive crossover network. The lower horns allows the installer/designer the capability to give that “brightening splash” of sound to those first few rows (especially outer edges). A 16 gauge steel grill or an optional decorative cloth grill and frame are available on this cabinet.

Construction

For structural integrity ¾” void free birch veneer plywood is used. Top and side panels are internally reinforced with “steel” angle braces making the cabinet structurally engineered for flying. In addition all joints are reinforced with internal wood bracing both glued and cross-nailed in place.

# SL1-200 DF Application

# The SL1-200 DF is a two-way passive Loudspeaker that uses a 12” woofer and a 1“ high frequency drivers coaxially mounted in asymmetrical horns (110 degree horizontal x 15 degree upper vertical x 45 degree lower vertical). Two 90 degree H x 60 degree V horn and 1” exit driver assemblies (actively controlled) mounted to adjustable brackets for down fill coverage. The SL1-200 DF should be used whenever high intelligibility and maximum pattern control is needed for speech and music sound reinforcement. The SL1-200 DF can be used alone but works excellently when additional low frequency is added either with the uniquely designed SL1-118 flyable subwoofer, or a floor positioned OAP SFT-115, OAP LF-115, OAP LF-118, OAP TR-215 or OAP TR-218.

# Flying Hardware Option

# Warning!!!!  Rigging and Flying of the SL1-200 DF should be done by persons familiar with standard rigging practices. If you are not familiar please consult the factory, your Dealer, the local Stage Hands Union, or a Rigging Supply Company in your area.

# The SL1-200 DF is easily flyable using the four rigging points on the top and/or the sides and rear of the cabinet. A 3/8” x 16 x 1 ½” Forged I-bolt (SL1-FIB) is available for use in attaching “flying” support cables to the cabinet to the fly points.

# Architectural Specifications

# The loudspeaker shall be of the two-way type. The sides of the enclosure shall be perpendicular to the top and the bottom of the enclosure. The upper panel of the front baffle (housing for the Coaxial Asymmetrical horns and drivers) will be parallel to the rear panel. The high frequency device shall incorporate a 1” exit throat asymmetrical horn (110 degree horizontal x 15 degree in the upper vertical x 45 degree in the lower vertical) coupled to a 1” exit high frequency driver. The Mid Frequency Asymmetrical Horn will be coupled to a 12” woofer. The loudspeaker shall have two additional 1” exit horns mounted to the bottom of the enclosure on an adjustable mount that is capable of 120 degree vertical rotation. The lower horns will supplement potential front-fill requirements. The lower horns will each have a constant directivity dispersion of 90 degrees horizontal x 60 degrees vertical. Input connection to the system shall be located on the rear of the enclosure and shall be two two-position barrier strip type. One for the Mid Hi portion of the Loudspeaker and one for the Downfill Speakers. A 16 gauge perforated steel grill or an optional fabric covered grill frame will be provided. Ease of access to the components of the system is facilitated for field serviceability. The Loudspeaker shall be the OAP SL-1 Series model SL1-200 DF.

# Décor Matching

The enclosure will have the finish deliverable options of “unfinished” (for future staining), “black textured enamel paint”, or “white textured enamel paint”. Additionally, the unit can be manufactured with a 16 gauge perforated steel grill (black or white) or optional cloth grill in black, white, wheat, or pumice.

# Warranty

OAP Audio SL1-200 DF Model Loudspeakers are guaranteed against failure due to workmanship and materials for a period of five years from the date of purchase and is limited to the original purchaser. If such failure does occur, the unit will be replaced or repaired (at the discretion of OAP Audio) without charge for labor and materials. The unit must be delivered to OAP Audio or one of its authorized service facilities prepaid. In-warranty items will be returned prepaid. Items not covered by warranty include: finish or appearance items, burned coils, or failures due to operation under other than specified conditions. This warranty also does not include any incidental or consequential damages. Repair by someone other than OAP Audio or an authorized OAP service facility will void this guarantee.

As a Research and Development Corporation, OAP Audio reserves the right to change specifications to improve performance.

# Specifications

## Impedance			8 ohm nominal

## Frequency Response		65 Hz – 20 KHz

## Power Handling			400 Watt Program Power

## Sensitivity			98 dB @ 1 watt / 1 meter (2.83V @ 1m)

Dimensions			25 ¼” W x 32” H x 16.5” D

Weight				70 lbs.

Low Freq. Device		12“ Woofer w/ 3” voice coil; 80 oz. Magnet

High Freq. Drivers		1” exit w/ 1.75” voice coil diameter, Mylar diaphragm

Asymmetrical Horns		110 hor.  x 15 upper vert.  x 45 lower vert.

Lower Adj. Horn 		(2) 90 degree horizontal  x 16 degree vertical

Crossover Freq.			1.6 KHz

Fly Points (3/8” x 16)		4 on top; 4 on upper sides

Cabinet Finish			Unfinished; White or Black Textured Enamel

Grill				16 Ga. Perf. Steel – White or Black; Cloth option

White, Black, Wheat, Pumice

Input				(2) 2 position Barrier Strips